## Slide 1: CPU cache
임종범
jblim@kpu.ac.kr

## Slide 2: Layering and Interfaces
Application Programming Interface (API), Application Binary Interface (ABI), and Instruction Set Architecture (ISA).
An application uses library functions (A1), makes system calls (A2), and executes machine instructions (A3)

## Slide 3: Interfaces
Instruction Set Architecture (ISA) – at the boundary between hardware and software.
Application Binary Interface (ABI) – allows the ensemble consisting of the application and the library modules to access the hardware; the ABI does not include privileged system instructions, instead it invokes system calls.
Application Program Interface (API) - defines the set of instructions the hardware was designed to execute and gives the application access to the ISA; it includes high-level language (HLL) library calls which often invoke system calls

## Slide 4: cache and main memory

## Slide 5: cache and main memory

## Slide 6: cache and main memory Example: Intel Core i7 (old model)
64-bit processor, x86-64 instruction set
  36-bit physical addresses and 48-bit virtual addresses
Three-level cache hierarchy; all levels use 64-byte block size; two-level TLB
  L1 cache:
    I cache: 32 KB 4-way set associative; D cache: 32 KB 8-way set associative; per core, pseudo LRU replacement, virtually indexed and physically tagged
  L2 cache:
    256 KB, 8-way set associative, per core, pseudo-LRU replacement, physically indexed
  L3 cache:
    2 MB per core, 16-way set associative, pseudo-LRU replacement (with ordered selection algorithm), physically indexed
  First-level TLB:
    I TLB: 128 entries, 4-way set associative, pseudo-LRU replacement; D TLB: 64 entries, 4-way set associative, pseudo-LRU replacement
  Second-level TLB:
    512 entries, 4-way set associative, pseudo-LRU replacement, 4 KB page size

## Slide 7: CPU Pipelines (Sandy Bridge)

## Slide 8: microcode for movsb (AMD)
movsb (move byte string)
1. LDDF ; load directioni flag to latch in funtional unit
2. OR ecx, ecx ; test if ECX is zero
3. JZ end ; terminate string move if ECX is zero
loop:
4. MOVFM+ tmp0, [esi] ; move to tmp data from source and inc/dec ESI
5. MOVTM+ [edi], tmp0 ; move the data to destination and inc/dec EDI
6. DECXJNZ loop ; dec ECX and repeat until zero
end:
7. EXIT

## Slide 9: A Typical Memory Hierarchy
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
On-Chip Components
L2 (Second
Level)
Cache
CPU Core
Secondary
Storage
(Disk)
Reg File
Main
Memory
(DRAM)
ITLB
DTLB
L1I (Instr Cache)
L1D (Data Cache)

## Slide 10: How is the Hierarchy Managed?
Who manages data transfer between
  Main memory  Disks
    by the operating system (virtual memory)
    by the programmer (files)
  Registers  Main memory
    by compiler (and programmer)
  Cache  Main memory
    by hardware (cache controller)
DDR3
HDD
Pentium
(1993)

## Slide 11: Basic Cache Operation
Main Memory
(DRAM)
Processor
address
data
CPU
Cache
CPU
TAG (Address)
D0
D1
D2
D3
...
...
...
...
...
...
11111111
22222222
33333333
44444444
55555555
66666666
77777777
88888888
99999999
12121212
23232323
34343434
Memory
0x0000
0x0004
0x0008
0x000C
0x1200
0x1204
0x1208
0x120C
0x1210
0x1214
0x1218
0x121C
0x0000_0004
11111111
22222222
33333333
44444444
0x0000_0
0x0000_000C
22222222
44444444
0x0000_1208
55555555
66666666
77777777
88888888
0x0000_1
77777777
Cache line (block)
(4 words in this example)
1023
1022
.
.
.
.
.
1
0

## Slide 12: Why Caches Work?
The size of cache is tiny compared to main memory
  How to make sure that the data CPU is going to access is in caches?
Caches take advantage of the principle of locality in your program
  Temporal Locality (locality in time)
    If a memory location is referenced, then it will tend to be referenced again soon. So, keep most recently accessed data items closer to the processor
  Spatial Locality (locality in space)
    If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon. So, move blocks consisting of contiguous words closer to the processor

## Slide 13: Example of Locality
int A[100], B[100], C[100], D;
for (i=0; i<100; i++) {
C[i] = A[i] * B[i] + D;
}
A[0]
A[1]
A[2]
A[3]
A[5]
A[6]
A[7]
A[4]
A[96]
A[97]
A[98]
A[99]
B[1]
B[2]
B[3]
B[0]
. . . . . . . . . . . . . .
B[5]
B[6]
B[7]
B[4]
B[9]
B[10]
B[11]
B[8]
C[0]
C[1]
C[2]
C[3]
C[5]
C[6]
C[7]
C[4]
. . . . . . . . . . . . . .
. . . . . . . . . . . . . .
C[96]
C[97]
C[98]
C[99]
D
A Cache Line (block)
Cache

## Slide 14: Example of Locality
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char *argv[]) {
int i, j, k, loops;
int a[2000] = { 0 };
int b[2000][1000] = { 0 };
int c[2000] = { 0 };
if (argc != 2) {
fprintf(stderr, "usage: ./loop <loops>\n");
return 1;
}
loops = atoi(argv[1]);
for (k = 0; k < loops; k++)
for (i = 0; i < 2000; i++)
for (j = 0; j < 1000; j++)
a[i] = a[i] + b[i][j] * c[i];
return 0;
}

## Slide 15: Cache Terminology
Block (cache line): the minimum unit of data present in a cache
  For example, 64B block in modern CPUs
Hit: if the requested data is in cache, it is called a hit
  Hit rate: the fraction of memory accesses found in caches
    For example, CPU requested data from memory, and cache was able to supply data 90% of the requests. Then, the hit rate of the cache is 90%
  Hit time: the time required to access the data found in cache
Miss: if the requested data is not in cache, it is called a miss
  Miss rate: the fraction of memory accesses not found in cache (= 1 - Hit Rate)
  Miss penalty: the time required to fetch a block into a level of the memory hierarchy from the lower level

## Slide 16: Direct-mapped Cache
The simplest cache structure: Direct mapped cache
  Each memory block is mapped to exactly one block in cache
    Lots of memory blocks must share a block in cache
  Address mapping to cache
    (block address) modulo (# of blocks in cache)
  Have a tag associated with each cache block that contains the address information
    The tag is the upper portion of the address required to identify the block
Data
Tag
Valid
Cache line
(=block)
11
11
00
10
01
11
00
10

## Slide 17: Memory Address
Cache
CPU Core
address
data
31 30 . . . . . . 8 7 6 5 4 3 2 1 0
Address from CPU
Byte Address
Word (4B) Address
Block (16B) Address
Block (64B) Address
Block (32B) Address

## Slide 18: Direct-mapped Cache
    Mapping to cache
      (block address) modulo (# of blocks in the cache)
    Cache structure
      Data: actual data
      Tag: which block is mapped to the cache?
      Valid: Is the block in the cache valid?
Data
Tag
Valid

## Slide 19: Example
4KB direct-mapped cache with 1 word (32-bit) blocks
Data
Tag
Valid
Index
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
20
10
Index
20
Tag
Hit
32
Data
Address from CPU
Cache
CPU Core
address
data
4B

## Slide 20: Example: DM$, 8-Entry, 4B blocks
Assume that address bus from CPU is 8-bit wide
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d

## Slide 21: Example: DM$, 8-Entry, blocks:4B
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#24 is 0001 1000
4-byte block, drop low 2 bits for byte offset! Only matters for byte-addressable systems
Index = log2(8) bits
3
Index
0
0
0
0
0
0
0
0
Cache miss!

## Slide 22: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#24 is 0001 1000
Index
0
0
0
0
0
0
0
0
a
000
1
To CPU (a)

## Slide 23: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#28 is 0001 1100
Index
0
0
0
0
0
0
0
a
000
1
b
000
1
Cache miss!
To CPU (b)

## Slide 24: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#60 is 0011 1100
Index
0
0
0
0
0
0
a
000
1
b
000
1
It’s valid! Is it a hit or a miss?

## Slide 25: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#60 is 0011 1100
Index
0
0
0
0
0
0
a
000
1
b
000
1
The tags don’t match! It’s not what we want to access!
Cache Miss!

## Slide 26: Example: DM$, 8-Entry, 4B blocks
b
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#60 is 0011 1100
Index
0
0
0
0
0
0
a
000
1
c
001
1
Do we have to bring the block to the cache and write to cache?
Let’s assume that (it’s called write-allocation policy)
000

## Slide 27: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c
d
#60 is 0011 1100
Index
0
0
0
0
0
0
a
000
1
new value ($3)
001
1
Do we update memory now? Or later?
Assume later (it is called write-back cache)
Now, we can write a new value to the location
c

## Slide 28: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c (old)
d
0
0
0
0
0
0
a
000
1
new value ($3)
001
1
How do we know which blocks in cache need to be written back to main memory?
Dirty
0
0
0
0
0
0
1
0
Need extra state! The “dirty” bit!

## Slide 29: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
c (old)
d
#188 is 1011 1100
Index
0
0
0
0
0
0
a
000
1
new value ($3)
001
1
Dirty
0
0
0
0
0
0
1
0
Cache miss!

## Slide 30: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
new value ($3)
d
#188 is 1011 1100
Index
0
0
0
0
0
0
a
000
1
new value ($3)
001
1
Dirty
0
0
0
0
0
0
1
0
Dirty bit is set!
So, we need to write the block to memory first
c (old)

## Slide 31: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
new value ($3)
d
#188 is 1011 1100
Index
0
0
0
0
0
0
a
000
1
d
101
1
Dirty
0
0
0
0
0
0
0
0
Now, we can bring the block to the cache
new value ($3)
001

## Slide 32: Example: DM$, 8-Entry, 4B blocks
Main Memory
  lw $1, 24($0)
  lw $2, 28($0)
  sw $3, 60($0)
  sw $4, 188($0)
24
Address
28
60
188
Cache (32B)
Valid
Tag
Data
Index
0
1
2
3
4
5
6
7
a
b
new value ($3)
d (old)
#188 is 1011 1100
Index
0
0
0
0
0
0
a
000
1
new value ($4)
101
1
Dirty
0
0
0
0
0
0
0
1
Now, we can write a new value to the location
d

## Slide 33: Handling Writes
When it comes to a read miss, we bring the block to cache and supply data to CPU
When it comes to a write miss, there are options you can choose from
  Upon a write-miss,
    Write-allocate: bring the block into cache and write
    Write no-allocate: write directly to main memory w/o bringing the block to the cache
  When writing,
    Write-back: update values only to the blocks in the cache and write the modified blocks to memory (or the lower level of the hierarchy) when the block is replaced
    Write-through: update both the cache and the lower level of the memory hierarchy
Write-allocate is usually associated with write-back policy
Write no-allocate is usually associated with write-through policy

## Slide 34: Write-Allocate & Write-back
Main Memory
(DRAM)
Processor
address
data
CPU
Cache
CPU
TAG (Address)
D0
D1
D2
D3
...
...
...
...
...
...
11111111
22222222
33333333
44444444
55555555
66666666
77777777
88888888
99999999
12121212
23232323
34343434
memory
0x0000
0x0004
0x0008
0x000C
0x1200
0x1204
0x1208
0x120C
0x1210
0x1214
0x1218
0x121C
0x0000_0004
11111111
22222222
33333333
44444444
0x0000_0
0x0000_1208
55555555
66666666
77777777
88888888
0x0000_1
Cache line (block)
(4 words in this example)
V
D
...
...
1
1
12345678
1
1
dddddddd
Allocate first upon a write miss

## Slide 35: Write No-allocate & Write-through
CPU
...
...
...
...
...
...
11111111
22222222
33333333
44444444
55555555
66666666
77777777
88888888
99999999
12121212
23232323
34343434
memory
0x0000
0x0004
0x0008
0x000C
0x1200
0x1204
0x1208
0x120C
0x1210
0x1214
0x1218
0x121C
0x0000_0004
0x0000_1208
55555555
66666666
77777777
88888888
0x0000_1
Cache line (block)
(4 words in this example)
...
1
12345678
dddddddd
Do not allocate to cache upon a write miss
12345678
Main Memory
(DRAM)
Processor
address
data
CPU
Cache
TAG (Address)
D0
D1
D2
D3
V

## Slide 36: Hits vs. Misses
Read hits
  This is what we want!
Read misses
  Stall the CPU, fetch the corresponding block from memory, deliver to cache and CPU, and continue to run CPU
Write hits
  Write-through cache: write data to both cache and memory
  Write-back cache: write the data only into the cache and set the dirty bit (and write the block to memory later when replaced)
Write misses
  Write-allocate with write-back: read the block into the cache, then write the word only to the cache
  Write no-allocate with write-through: write the word only to the main memory (w/o bringing the block to cache)
Main Memory
(DRAM)
Processor
address
data
CPU
Cache

## Slide 37: Direct Mapped Cache (4-word Block)
Cache size = 4KB
Data (4 words = 16B)
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 3 2 1 0
Byte offset
20
Block offset
Data
32
Index
8
20
Tag
Hit
block address

## Slide 38: Miss Rate vs Block Size vs Cache Size
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller
  Stated alternatively, spatial locality among the words in a word decreases with a very large block; Consequently, the benefits in the miss rate become smaller
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6

## Slide 39: Cache Hardware Cost
How many total bits are required for a direct mapped data cache with 16KB of data and 4-word blocks assuming a 32-bit address?
Data
Tag
V
D
0
1
2
.
.
.
1021
1022
1023
Byte offset (2 bits)
Block offset (2 bits)
Index (10 bits)
31 30 . . . 15 14 13 . . . 4 3 2 1 0
Address from CPU
tag (18 bits)
  #bits = #blocks x (block size + tag size + valid size + dirty size)
  = 1024 x (16B + 18 bits + 1 bit + 1 bit)
  = 148 Kbits = 18.5 KB
  15.6% larger than the storage for data
block address
(4 words = 16B)

## Slide 40: Reducing Cache Miss Rates (#1)
Alternatives for more flexible block placement
  Direct mapped cache maps a memory block to exactly one location in cache
  Fully associative cache allows a memory block to be mapped to any cache block
  N-way set associative cache divides the cache into sets, each of which consists of n different locations (ways)
    A memory block is mapped to a unique set (specified by the index field) and can be placed in any way of that set (so, there are n choices)

## Slide 41: Associative Cache Example
2-way
4 sets
Only 1 set
8 sets

## Slide 42: Spectrum of Associativity
For a cache with 8 entries

## Slide 43: 4-Way Set Associative Cache
16KB cache
  4B (32-bit) per block
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
.
1022
1023
Data
Tag
V
0
1
2
.
.
.
.
1022
1023
Data
Tag
V
0
1
2
.
.
.
.
1022
1023
Data
Tag
V
Index
0
1
2
.
.
.
.
1022
1023
10
Index
20
Tag
32
Data
4x1 mux
Hit
Way 0
Way 1
Way 2
Way 3
32
32
32
block address

## Slide 44: Associative Caches
Fully associative
  Allow a memory block to go in any cache entry
  Requires all cache entries to be searched
  Comparator per entry (expensive)
N-way set associative
  Each set contains N entries
  (Block address) % (#sets in cache) determines which set to search
  Search all n entries in a indexed set
  n comparators (less expensive)

## Slide 45: Associativity Example
Assume that there are 3 small different caches with 4 one-word blocks, and CPU generates 8-bit address to cache
  Direct mapped
  2-way set associative
  Fully associative
Find the number of misses for each cache organization given the following sequence of block addresses: 0, 8, 0, 6, 8
  We assume that the sequence is for all memory reads (lw)
Notes: In 2013, change from block address to byte address and add that CPU is executing 5 different lw instructions.

## Slide 46: Associativity Example
Direct mapped cache
Data
Tag
V
0
1
2
3
0, 8, 0, 6, 8
Index
0
0
7 6 5 4 3 2 1 0
Tag
Index
0000
Byte address | Block address | Cache Index | Hit or Miss?
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0001 1000 (0x18) | b’00 0110 (0x06) | 2 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
Mem[0]
tag
miss
miss
miss
miss
miss
Mem[8]
Mem[0]
Mem[8]
Mem[6]
0010
0000
0001
0010
8
0
8
6
0
0
0
1
1
block address

## Slide 47: Associativity Example (Cont')
2-way set associative
Data
Tag
V
0
1
0, 8, 0, 6, 8
Index
0
0
Tag
Index
00000
Byte address | Block address | Cache Index | Hit or Miss?
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0001 1000 (0x18) | b’00 0110 (0x06) | 0 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
Mem[0]
tag
miss
miss
hit
miss
miss
Mem[8]
Mem[8]
Mem[6]
00100
00011
00100
8
0
8
6
0
1
Data
Tag
V
0
0
1
block address
7 6 5 4 3 2 1 0

## Slide 48: Associativity Example (Cont)
Fully associative
Data
Tag
V
0
0, 8, 0, 6, 8
Index
0
0
7 6 5 4 3 2 1 0
Tag
000000
Byte address | Block address | Cache Index | Hit or Miss?
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
b’0000 0000 (0x00) | b’00 0000 (0x00) | 0 | 
b’0001 1000 (0x18) | b’00 0110 (0x06) | 0 | 
b’0010 0000 (0x20) | b’00 1000 (0x08) | 0 | 
Mem[0]
tag
miss
miss
hit
miss
hit
Mem[8]
Mem[6]
001000
000110
8
0
8
6
1
Data
Tag
V
0
1
Data
Tag
V
0
Data
Tag
V
0
1
block address

## Slide 49: Benefits of Set Associative Caches
The choice of direct mapped or set associative depends on the cost of a miss versus the cost of implementation
Largest gains are achieved when going from direct mapped to 2-way (more than 20% reduction in miss rate)

## Slide 50: Range of Set Associative Caches
For a fixed size cache, the increase by a factor of 2 in associativity doubles the number of blocks per set (the number of ways) and halves the number of sets
  Example: An increase of associativity from 4 ways to 8 ways decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
Block offset and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity
Selects the set
Used for tag comparison
Selects the word in the block
address
Block address

## Slide 51: Replacement Policy
Upon a miss, which way’s block should be picked for replacement?
  Direct mapped cache has no choice
  Set associative cache prefers non-valid entry if there is one. Otherwise, choose among entries in the set
    Least-recently used (LRU)
      Choose the one unused for the longest time
      Hardware should keep track of when each way’s block was used relative to the other blocks in the set
      Simple for 2-way (takes one bit per set), manageable for 4-way, too hard beyond that
    Random
      Gives approximately the same performance as LRU with high-associativity cache

## Slide 52: Example Cache Structure with LRU
2-way set associative data cache
Data
Tag
V
Data
Tag
V
D
D
LRU
Set 0
Set 1
Set 2
…
Set n-3
Set n-2
Set n-1
Way 0
Way 1
LRU

## Slide 53: Reducing Cache Miss Penalty (#2)
Use multiple levels of caches
  Primary cache (Level-1 or L1) attached to CPU
    Small, but fast
  Level-2 (L2) cache services misses from primary cache
    Larger, slower, but faster than L3
  Level-3 (L3) cache services misses from L2 cache
    Largest, slowest, but faster than main memory
  Main memory services L3 cache misses
Advancement in semiconductor technology allows enough room on the die for L1, L2, and, L3 caches
  L2 and L3 caches are typically unified, meaning that it holds both instructions and data
CPU Core
Reg File
L1 I$ (32KB)
L1 D$ (32KB)
L3 Cache (8MB)
L2 Cache (256KB)
Memory

## Slide 54: Core i7 Example
Core i7
L2 Cache (256KB)
CPU Core
Reg File
L1 I$ (32KB)
L1 D$ (32KB)
L3 Cache (8MB) - Shared
L2 Cache (256KB)
CPU Core
Reg File
L1 I$ (32KB)
L1 D$ (32KB)
..

## Slide 55: Virtualization - VT-x / AMD-V
임종범
jblim@kpu.ac.kr

## Slide 56: What is virtualization?
Virtualization refers to the act of creating a virtual (rather than actual) version of something, including a virtual computer hardware platform, operating system (OS), storage device, or computer network resources
Hardware virtualization or platform virtualization refers to the creation of a virtual machine that acts like a real computer with an operating system

## Slide 57: Hardware virtualization
Major types of hardware virtualization include:
  Full virtualization
    almost complete simulation of the actual hardware to allow software, which typically consists of a guest operating system, to run unmodified
  Paravirtualization
    a hardware environment is not simulated; however, the guest programs are executed in their own isolated domains, as if they are running on a separate system
    Guest programs need to be specifically modified to run in this environment

## Slide 58: Software based techniques
Binary translation
  Emulation of one instruction set by another for same CPU.
  When source and target instruction set are the same, it’s called instruction set simulation
  can be done “just in time” (JIT)
    can do some caching to be more efficient (i.e., hot spot detection)
Para-virtualization
  modification of guest kernel to support being virtualized
  Can be pretty efficient

## Slide 59: Binary Translation
x86 assembly cannot be virtualized because some privileged instructions don’t generate exceptions
Workaround: translate the unsafe assembly from the guest to safe assembly
  Known as binary translation
  Performed by the VMM
  Privileged instructions are changed to function calls to code in VMM

## Slide 60: Binary Translation Example
Guest OS Assembly
do_atomic_operation:
cli
mov eax, 1
xchg eax, [lock_addr]
test eax, eax
jnz spinlock
…
…
mov [lock_addr], 0
sti
ret
Translated Assembly
do_atomic_operation:
call [vmm_disable_interrupts]
mov eax, 1
xchg eax, [lock_addr]
test eax, eax
jnz spinlock
…
…
mov [lock_addr], 0
call [vmm_enable_interrupts]
ret

## Slide 61: Binary translation – example
vEPC
mov ebx, eax
cli
and ebx, ~0xfff
mov ebx, cr3
sti
ret
mov ebx, eax
mov [VIF], 0
and ebx, ~0xfff
mov [CO_ARG], ebx
call HANDLE_CR3
mov [VIF], 1
test [INT_PEND], 1
jne
call HANDLE_INTS
jmp HANDLE_RET
start
Guest Code
Translation Cache
Source: Carl Waldspurger, Introduction to Virtual Machines
Notes: Source: http://labs.vmware.com/academic/mit-iap-2010

## Slide 62: Hypervisor
A hypervisor or virtual machine monitor (VMM) is a piece of computer software, firmware or hardware that creates and runs virtual machines
A computer on which a hypervisor is running one or more virtual machines is defined as a host machine
Each virtual machine is called a guest machine
The hypervisor presents the guest operating systems with a virtual operating platform and manages the execution of the guest operating systems
Multiple instances of a variety of operating systems may share the virtualized hardware resources.

## Slide 63: Hypervisor
Linux
Windows
OS X
Hypervisor
(Virtual Machine Monitor)
Virtual
Machine
Virtual
Machine
Virtual
Machine
Platform
(CPU, Memory, IO, etc)
Host
Guest

## Slide 64: Hypervisor
Type-1: native or bare-metal hypervisors
  run directly on the host's hardware to control the hardware and to manage guest operating systems
Type-2: hosted hypervisors
  run on a conventional operating system just as other computer programs do

## Slide 65: Hardware-assisted virtualization
Hardware-assisted virtualization
  A way of improving overall efficiency of virtualization
  It involves CPUs that provide support for virtualization in hardware, and other hardware components that help improve the performance of a guest environment.

## Slide 66: Vendor technologies
 | Intel | AMD
CPU Flag | Virtual Machine Extensions (VMX) | Secure Virtual Machine (SVM)
Processor emulation | VT-x | AMD-v
Extended page tables | Extended page tables (EPT) | Rapid Virtualization Indexing (RVI)
MMU emulation | VT-d | AMD-Vi
Network emulation | VT-c | 
PCI emulation | PCI-SIG I/O Virtualization | PCI-SIG I/O Virtualization
We will be focused on Intel VT-x
Notes: We will primarily be covering VT-x, but most of it maps to AMD-v as well.

## Slide 67: Checking The 64-bit feature
Use CPUID input-value 0x80000001 for obtaining extended feature bits
Returned in the ECX and EDX registers
.data
ext_features DB 8 DUP(0) # 8 bytes (zeroed) for extended features bits
.code
mov eax, 80000001h # setup input-value in EAX
cpuid # then execute CPUID
mov [ext_features+0], edx # save feature-bits from EDX
mov [ext_features+4], ecx # save feature-bits from ECX

## Slide 68: Extended features bits
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
L
S
F
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
R
R
IA32e
R
R
R
R
R
R
R
R
X
D
R
R
R
R
R
R
R
R
S
Y
S
C
A
L
L
R
R
R
R
R
R
R
R
R
R
R
31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
ECX =
EDX =
IA32e = Intel 64-bit Technology
XD = eXecute Disable paging-bit implemented
SYSCALL = Fast SYSCALL / SYSRET (64-bit mode)
LSF = LAHF / SAHF implemented in 64-bit mode
R = reserved bit

## Slide 69: New instructions (x64)
CDQE | Convert doubleword to quadword
CMPSQ | Compare string operands
CMPXCHG16B | Compare RDX:RAX with m128
LODSQ | Load qword at address (R)SI into RAX
MOVSQ | Move qword from address (R)SI to (R)DI
MOVZX (64-bits) | Move doubleword to quadword, zero-extension
STOSQ | Store RAX at address RDI
SWAPGS | Exchanges current GS base register value with value in MSR address C0000102H
SYSCALL | Fast call to privilege level 0 system procedures
SYSRET | Return from fast system call
Notes: No need to memorize these, just something to keep in mind.

## Slide 70: New instructions for virtualization

## Slide 71: Hardware-assisted virtualization
Privilege ring
OS
Apps
Apps
Apps
Apps
Ring 0
Ring 3
VMM
Ring 0
VMX Non-Root Mode
VMX Root Mode
VM Exit
MOV CR, RDMSR, WRMSR
VMX Non-Root:
  Operation restricted
  Certain instructions cause a VM Exit
  Certain events cause a VM Exit
VMX Root:
  Full control over the processor
  Some new instructions
Guest

## Slide 72: Hardware-assisted virtualization
Privilege ring
OS
Apps
Apps
Apps
Apps
Ring 0
Ring 3
VMM
Ring 0
VMX Non-Root Mode
VMX Root Mode
Ring 0
Ring 1
Ring 2
Ring 3
Guest
Ring -1
Ring -1
VMX Root Mode is a new protection level added for virtualization

## Slide 73: Hardware-assisted virtualization
Privilege ring
OS
Apps
Apps
Apps
Apps
Ring 0
Ring 3
VMM
Ring 0
VMX Non-Root Mode
VMX Root Mode
Ring 0+
(Virtual Ring 0)
Ring 1+
(Virtual Ring 1)
Ring 2+
(Virtual Ring 2)
Ring 3+
(Virtual Ring 3)
Guest
Ring 0
VMX Root Mode is a new protection level added for virtualization

## Slide 74: Hardware-assisted virtualization
Virtual Machine Control Structure (VMCS)
OS
Apps
Apps
Apps
Apps
Ring 0+
Ring 3+
VMM
Ring 0
VMX Non-Root Mode
VMX Root Mode
Guest
VMCS
VM Exit
VM Entry
A VMCS defines the behavior of operation when in VMX Non-Root mode and manages transitions into and out of VMX Non-Root mode
Defined sections:
  Guest State Area
  Host State Area
  VM Execution Control
  VM Entry Control
  VM Exit Control
  VM Exit Information
Up to a 4Kbyte structure
  read/write by VMREAD/VMWRITE ops.

## Slide 75: Hardware-assisted virtualization
Active Guest
Idle Guest
Hypervisor
(VMM)
VMPTRLD
VMLAUNCH
OS
Apps
Apps
Apps
Virtual Processor
OS
Apps
Apps
Apps
Virtual Processor
Core 0
VMX Root Mode
VMCS
VMCS
VMXON
VMCS
VMX Non-Root Mode
VM Exit

## Slide 76: Hardware-assisted virtualization
Active Guest
Idle Guest
Hypervisor
(VMM)
VMRESUME
VMCLEAR
OS
Apps
Apps
Apps
Virtual Processor
OS
Apps
Apps
Apps
Virtual Processor
Core 0
VMX Root Mode
VMCS
VMCS
VMXON
VMCS
VMX Non-Root Mode
VM Exit

## Slide 77: Hardware-assisted virtualization
Active Guest
Idle Guest
Hypervisor
(VMM)
VMPTRLD
VMLAUNCH
OS
Apps
Apps
Apps
Virtual Processor
OS
Apps
Apps
Apps
Virtual Processor
Core 0
VMX Root Mode
VMCS
VMCS
VMXON
VMX Non-Root Mode
VMCS
Active Guest
Idle Guest

## Slide 78: Virtualization - memory management
임종범
jblim@kpu.ac.kr

## Slide 79: IA32e Page Table Walk Process
Target Page
(4KB each)
Page
Table
63 0
CR3
63 0
Page
Directory
63 0
Page Directory
Pointer Table
63 0
Page Map
Level 4
63 0
Page Directory Index
(1 of 512)
Page Table Index
(1 of 512)
2120 12
Location within Page
(1 of 4096)
11 0
PDP Index
(1 of 512)
3029
PML4 Index
(1 of 512)
47 3938
Sign
Extended
63

## Slide 81: Native System Memory Management Unit Diagram

## Slide 82: Shadow Page Tables Diagram
VMM maintains PPN->MPN mappings in its internal data structures and stores LPN->MPN mappings in shadow page tables that are exposed to the hardware.
Recently used LPN->MPN translations are cached in the hardware TLB.
VMM keeps these shadow page tables synchronized to the guest page tables.
This synchronization introduces virtualization overhead when the guest updates its page tables.

## Slide 83: Second Level Address Translation
AMD-V and VT-x help the VMM control guests
… but, they don’t address the need for shadow page tables
Second level address translation (SLAT) allows the MMU to directly support guest page tables
  Intel: Extended Page Tables (EPT)
  AMD: Rapid Virtualization Indexing (RVI)
  Also known as Two Dimensional Paging (TDP)
  Introduced in 2008

## Slide 84: SLAT Implementation
VMM installs first and second level tables in the MMU
  Context switch to the guest via vmenter
Steps to translate an address:
  MMU queries the level 1 (guest) table
  MMU queries the level 2 (VMM) table
If any step yields an invalid PTE than page fault to the VMM (vmexit)
CPU

## Slide 85: Advantages of SLAT
Huge performance advantages vs. shadow page tables
When guests mov cr3, the CPU updates vmcr3 register
  No need to vmexit when guest OS switches context
EPT can be filled on-demand or pre-initialized with PFNMFN entries
  On-demand:
    Slower, since many address translations will trigger hidden misses
    … but hardware pages for the guest can be allocated when needed
    And, the EPT will be smaller
  Preallocation:
    No need to vmexit when the guest OS creates or modifies it’s page tables
    … but hardware pages need to be reserved for the guest
    And, the EPT table will be larger

## Slide 86: Hardware Memory Management Unit Diagram

## Slide 87: Hardware Memory Management Unit Diagram
Guest maintain LPN->PPN mappings in the guest page tables
VMM maintains PPN->MPN mappings called nested page tables
Both the guest page tables and the nested page tables are exposed to the hardware.
When a logical address is accessed, the hardware walks the guest page tables as in the case of native execution,
For every PPN accessed during the guest page table walk, the hardware also walks the nested page tables to determine the corresponding MPN.
This composite translation eliminates the need to maintain shadow page tables and synchronize them with the guest page tables.
However the extra operation also increases the cost of a page walk, thereby impacting the performance of applications that stress the TLB.
This cost can be reduced by using large pages, thus reducing the stress on the TLB for applications with good spatial locality.

## Slide 90: Hardware-Assisted Page Walks
Two-dimensional page walks for virtualized systems
gL4
5
gL3
10
gL2
15
gL1
20
gCR3
gVA
Guest page table
(gLn)
nL4
6
nL3
7
nL2
8
nL1
9
nL4
11
nL3
12
nL2
13
nL1
14
nL4
16
nL3
17
nL2
18
nL1
19
nL4
21
nL3
22
nL2
23
nL1
24
sPA
nL4
1
nL3
2
nL2
3
nL1
4
nCR3
gPA (gL4)
sPA
gVA: guest virtual address
gPA: guest physical address
sPA: system physical address
Nested page table
(nLn)
x86_64

## Slide 91: Hardware-Assisted Page Walks
Two-dimensional page walks for virtualized systems
gL4
5
gL3
10
gL2
15
gL1
20
gCR3
gVA
Guest page table
(gLn)
nL4
6
nL3
7
nL2
8
nL1
9
nL4
11
nL3
12
nL2
13
nL1
14
nL4
16
nL3
17
nL2
18
nL1
19
nL4
21
nL3
22
nL2
23
nL1
24
sPA
nL4
1
nL3
2
nL2
3
nL1
4
nCR3
gPA (L4)
sPA
gVA: guest virtual address
gPA: guest physical address
sPA: system physical address
Nested page table
(nLn)
x86_64
Guest (m-levels) and nested (n-levels) page tables
# of page walks: mn + m + n
x86_64: 4*4 + 4 + 4 = 24

## Slide 92: Nested Paging
CPU maps each Guest_PA to Host_VA and then translates to Host_PA
CPU builds compound gVA_to_hPA TLB entries (guarded by ASID)

## Slide 93: TLB Hit
Hypervisor starts a guest with Nested Paging enabled
Guest reads from a memory location
vCPU locates memory in TLB
Memory is fetched from DRAM using system physical address in TLB

## Slide 94: TLB Miss
Hypervisor starts a guest with Nested Paging enabled
Guest reads from a memory location
vCPU does not locate memory in TLB
Processor walks Nested Page Tables

## Slide 95: Address space id (ASID)

## Slide 96: Tagged TLB
Each VM has a unique ASID value, known only to the hyper-visor and the TLB hardware.
The ASID is invisible to the guest OS, thus eliminating the need to modify the guest, preserving the virtual illusion and avoiding any performance degradation.

## Slide 97: Hardware support for Nested Paging
Page Walk Cache (PWC)
  AMD64 processors maintain a fast internal PWC for memory referenced by frequently used page table entries
Nested TLB (NTLB)
  To cache guest physical to system physical translations
  To reduce average # of page entry references during a nested walk

## Slide 98: Virtualization - Interrupt
임종범
jblim@kpu.ac.kr

## Slide 99: Interrupt Info
Interrupts can cause the currently executing program to be interrupted.
  Events that are asynchronous to program execution
    An interrupt request from a hardware device external to the processor is recognized if recognition of external interrupts is enabled (RFLAGS.IF=1)
    The assertion of the processor’s NMI (non-maskableinterrupt) input or the reception of an NMI, SMI, or INIT# IPI from the chipset
  Events that are synchronous to program execution
    Execution of a software interrupt (INT) instruction
    Processor detection of a software exception error condition
Most of these events are represented by an 8-bit Interrupt Vector
The Interrupt Vector is used to locate the correct Interrupt Handler (Interrupt Service Routine, ISR) to handle that specific event

## Slide 100: Programmable Interrupt Controller (PIC)

## Slide 101: Advanced PIC – APIC
Starting with the P54C version of the Pentium® processor, a Local APIC was incorporated in the processor
IO APIC(s) is (are) implemented as part of the chipsets

## Slide 102: Interrupt Delivery Via APIC Bus
This solution allowed the interrupt to target a specific processor, a group of processors, all processors, or the processor currently running the lowest-priority task (from the perspective of the OS)
This implementation also allowed a Local APIC to send an interrupt to another Local APIC or set of Local APICs

## Slide 103: Interrupt Delivery As Messages
In modern systems, IO based interrupts are now passed to the Local APIC via in-band messages
This architecture is often referred to as xAPIC
Intel Based System AMD Based System

## Slide 104: User-Defined Interrupts
Interrupt vectors 32-255 are free to be defined by software and possibly allocated to IO devices or allocated for the OS’s own purposes
Interrupt vectors 0-31 are reserved for x86 processor related interrupts and exceptions

## Slide 105: Priority of User-Defined Interrupts
User-Defined Interrupts are prioritized based on the upper 4 bits of their vector
Highest -Fxh
: -Exh
: - :
: -2xh
Lowest -1xh

## Slide 106: APIC Registers
IRR (Interrupt Request Register)
Processor
Core
Local APIC
Vector A1
(161 Decimal) ISR (In Service Register)
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
Bit 161
Bit 161
31 24 16 8 0
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 107: Multiple Interrupts in Process
IRR (Interrupt Request Register)
Processor
Core
Local APIC
ISR (In Service Register)
Bit 210
Bit 161
Bit 210
Vector D2
(210 Decimal)
Vector A1
(161 Decimal)
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 108: Multiple Interrupts in Process
IRR (Interrupt Request Register)
Processor
Core
Local APIC
ISR (In Service Register)
Bit 161
Bit 210
Not high
enough priority
Bit 93
Vector D2
(210 Decimal)
Vector 5D
(93 Decimal)
Vector A1
(161 Decimal)
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 109: End Of Interrupt (EOI)
IRR (Interrupt Request Register)
Processor
Core
Local APIC
ISR (In Service Register)
Bit 161
Bit 210
EOI
Bit 93
Traditional APIC behavior is to clear the highest priority interrupt that is in service
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 110: Interrupt Control
RFLAGS.IF enables / disables interrupts
  cli / sti instructions, or popf
Task Priority Register
  Processor TPR allows for control over the priority of interrupts that are permitted to interrupt the processor
APIC TPR provides the same functionality
APIC.TPR
Task
Priority
Sub-Class
Reserved
31 87 0
43
Task
Priority
Class
CR8.TPR
Reserved
63 43 0
Task
Priority
Class

## Slide 111: Interrupt Shadows
An interrupt cannot be taken at this point
Hardware defines a single instruction “shadow” where an interrupt will not be taken (ring 0 only)
The behavior is the same for pop ss
mov ax, value1
mov ss, ax
mov sp, value2

## Slide 112: Interrupts, Guests and Hypervisors
guest
kernel
hypervisor
hardware
interrupt
e.g.
timer tick
guest
kernel
guest
kernel
EOI
virtual
interrupt
(timer tick)
EOI
In current designs, all physical interrupts are for the hypervisor

## Slide 113: Interrupt Handling
The hypervisor chooses whether to intercept interrupts or to allow the guest to take physical interrupts
In the normal “multiple guest with hypervisor” scenario of today, the hypervisor mustintercept physical interrupts
  Just like an operating system scheduler, the hypervisor must regain control periodically, in order to schedule the guest (timer ticks)
Guest operating systems also need interrupts
  Virtual devices
  Periodic timer ticks for the guest operating system to use
Virtual Interrupts
  The hypervisor needs a mechanism to inject interrupts (and exceptions) into the guest

## Slide 114: Virtual VS. Physical Interrupts
Physical interrupt originates from a hardware device
Virtual interrupt is created by the hypervisor and injected into the guest
  End of Interrupt (EOI) should not be driven to the APIC!
  The APIC must be virtualized by the hypervisor or perhaps PIC mode

## Slide 115: APIC Virtualization
Device needed by guests (or perhaps PIC)
MMIO, use page table to trap guest accesses
Device emulation example
  Guest writes TPR to control interrupts
  Hypervisor knows whether to inject interrupts or not
guest
kernel
ring 0
hypervisor
hardware
Interrupts disabled
by the guest kernel
interrupt

## Slide 116: Software Model of the APIC
(Thin) Hypervisor
PC Platform
OS
Apps
OS DDs
Apps
DDs
OS
Console
DDs
Privileged
guest
Service
Operating
System
Virtualization Stack
Where does
the APIC
device model
belong?
The service operating is
good for breaking up the
logic, however it does add
overhead (latency) for
very high frequency
operations.

## Slide 117: Intel External Interrupts
VM-execution control offers a setting for interrupt behavior
  Either deliver the interrupt through the guest IDT, or
  Cause a VM-exit
Delivery of physical interrupts to the guest is controlled by RFLAGS.IF and the TPR
Guest execution must not interfere with VMM operation
  If interrupts are intercepted, the VM-exit occurs, ignoring guest RFLAGS.IF and ignoring guest TPR

## Slide 118: Intel APIC Virtualization
Virtual APIC page address. 4 Kbyte page for a virtual APIC
  Contains the TPR shadow that is read / written by mov CR8
TPR threshold
  If the TPR shadow falls below this value, VM exit
Typical guest activity is to write the TPR with an unchanged value. An exit is not required in this case

## Slide 119: Intel Event Injection
VM-Entry Interrupt Information Field
V: (valid) inject the event if the valid bit is set
E: deliver error code if the bit is set
Type:
0 = external interrupt
2 = NMI
3 = hardware exception
4 = software interrupt
5 = privileged software exception
6 = software exception
31 1110 87 0
V
E
Type
Vector

## Slide 120: Errors During Intel Event Injection
Delivery to the guest is using the guest IDT
Errors result in the appropriate guest IDT entry
  Vector is beyond the IDT limit
  Deliver a #GP to the guest
Subject to the exception bitmap
  If #GP is set to VM-exit, then event delivery will VM-exit

## Slide 121: Intel Interruptibility States
0001 | Blocking by RFLAGS.IF. External interrupts also can not be delivered to SMM
0010 | Blocking by interrupt shadow
0100 | Blocking by SMI. Further SMIs can not be delivered in SMM
1000 | Blocking by NMI. Delivery of NMI inhibits the delivery of further NMIs until IRET. NMI can not be delivered to SMM
Event injection overrides the interruptibilty
state for STI and interrupt shadow
Guest State -VMCS

## Slide 122: Intel Activity States
Active and HLT states block SIPIs (discarded)
Wait for SIPI blocks external interrupts, NMIs, SMIs, INIT
Shutdown blocks external interrupts and SIPIs
Guest State -VMCS
0 | Active | Normal execution
1 | HLT | Inactive : HLT executed
2 | Shutdown | Inactive : triple fault or other serious error
3 | Wait for SIPI | Inactive : Waiting for Startup IPI

## Slide 123: AMD Interrupt Virtualization
VMCB control bit to intercept interrupts
VMCB control bit V_INTR_MASKING
  Set :
    Guest interrupt enable flag (RFLAGS.IF) masks only virtual interrupts
    Guest accesses to the TPR (CR8) read / write the V_TPR
  Clear:
    Guest interrupt enable flag masks physical interrupts
    Guest CR8 writes modify the TPR

## Slide 124: AMD Interrupt Injection
The hypervisor creates a virtual interrupt – injects it into the guest
VMCB fields : (set by the hypervisor before vmrun invocation)
  V_IRQ: set to indicate a virtual interrupt is pending
  V_INTR_PRIO: priority for the virtual interrupt
  V_IGN_TPR: set to ignore the virtual TPR
  V_INTR_VECTOR: vector to use for this interrupt
    No cycle run to the APIC
  INTERRUPT_SHADOW: guest is in an interrupt shadow
Guest takes the interrupt, dependent on the guest virtual interrupt controls (TPR/IF)
  The guest might intercept before taking the interrupt

## Slide 125: AMD Event Injection
Event injection is a generic term for the injection of interrupts or exceptions
The hypervisor can create a virtual exception and inject it into the guest
VMCB fields: (set by the hypervisor before vmrun invocation)
  EVENTINJ
Guest takes the exception
  Not subject to the exception intercepts

## Slide 126: AMD Event Injection Information
V: (valid) set to 1 if the event is to be injected into the guest
EV:(error code valid) set to 1 if the error code should be pushed onto the stack
Type :
0 : Interrupt
2 : NMI
3 : Exception
4 : Software interrupt
The vmrun instruction will fail with an
error code if the supplied event injection
information is inconsistent. E.g., type 3
with a vector of 2 or with a vector > 31.
Error Code
32
0
63
31 1110 87
V
E
V
Type
Vector

## Slide 127: The need For The IER
IRR (Interrupt Request Register)
Processor
Core
Local APIC
ISR (In Service Register)
Bit 161
Bit 210
Processing of interrupt D2
(210) completed?
The APICbehavior would
be to clear EC (236)
This would be wrong!
Guest Y
Processing
interrupts:
D2 (210) and
A1 (161)
Guest X
Processing
interrupt:
EC (236)
Bit 236
Hypervisor timeslicing
guests on a single core
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 128: AMD APIC Use Of The IER
Delivery to the In
Service Register blocked
IRR (Interrupt Request Register)
Processor
Core
Local APIC
IER (Interrupt Enable Register)
Interrupt
4E (78) is
pending
Bit 78
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 129: EOI Subject To IER
IER (Interrupt Enable Register)
Processor
Core
Local APIC
ISR (In Service Register)
Bit 161
Bit 210
Processing of interrupt D2
(210) completed?
The APICbehavior would
be to clear EC (236)
This would be wrong!
Guest Y
Processing
interrupts:
D2 (210) and
A1 (161)
Guest X
Processing
interrupt:
EC (236)
Bit 236
D2 (210) cleared as EC (236) reset in IER
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 130: AMD End Of Interrupt
Traditional APIC behavior is to clear the highest priority pending interrupt
Does not work if guests directly own devices and process the interrupts
  Guest x may have interrupts disabled. The highest priority interrupt in APIC terms is for guest x
  Guest y has interrupts enabled, and is processing an interrupt that is lower priority in APIC terms
  EOI from guest y would clear the interrupt for guest x

## Slide 131: AMD Interrupt Enable Register
Hypervisor sets the IER mask on a per guest basis
Specific EOI added for clearing the pending interrupt
  Resides at 420h in APIC space
  Hypervisor can clear a targeted pending interrupt
ISR (In Service Register)
Bit 161
Bit 210Bit 236
31 24 16 8 0
0:31
63:32
95:64
127:96
159:128
191:160
223:192
255:224

## Slide 132: AMD EXITINTINFO
32
0
63
31 1110 87
Error Code
V
E
V
Type
Vector
V: (valid) set to 1 if the intercept occurred
while the guest was delivering an
exception through the IDT
EV:(error code valid) set to 1 if the error
code should be pushed onto the stack
Type :
0 : Interrupt
2 : NMI
3 : Exception
4 : Software interrupt